## Slide 1: Heterogeneous Hyperthreading Mingxuan He*, Fangping Liu†, Sang Wook Stephen Do† *Purdue University †Futurewei inc

## Slide 2: Heterogeneous Multicore
Heterogeneous CPU Architecture
  ARM  big.LITTLE
  Intel’s Alder Lake Architectures  Performance/efficiency cores
Threads can be schedule and migrated between cores
  Migration use coherent interconnect near the LLC
  In coarse granularity only
  Heterogeneous Architecture has demonstrated its effectiveness
LLC
Heterogeneous Multicore CPU Architectures Example
Performance Core
Efficiency cores

## Slide 3: Phases in Program and Dynamic Thread Assignment
Programs Exhibit Distinct Phases During Execution
  such as varying loops or regions within a loop.
These Phases Exhibit Different Performance Characteristics
  IPC may be comparable on P/E cores during certain phases.
Dynamic Thread Assignment at a Coarse Granularity
  Operating system reschedules threads every tens of milliseconds
  The performance difference between P/E cores is phase-dependent.
  Predict the performance of each threads on P/E-core
  Schedule on P/E-cores based on prediction to improve performance
  The scheduling mechanism aims to maintain fairness among threads.
  Opportunities in fine-grained phase is not captured

## Slide 4: Heterogeneous Single Core
Previous Works Deployed Heterogeneous in one core
  Each core has multiple backends – P/E
  Reschedule in fine-grained (In-core migration controller)
  Copy architecture status without coherent interconnect
  Scheduling window tens of milliseconds  1000s instrs
  Predict the performance in hardware for each window
  Schedule to Optimize Energy-Delay-Product (EDP)
Issue with Previous Heterogeneous Single Core
  Only one thread is scheduled (low utilization)
  One backend of CPU always idle
  Only optimize the EDP
  Needs to improve the pipeline utilization

## Slide 5: Opportunity of Heterogeneous Single Core
Heterogeneous Single Core v.s. Heterogeneous Multicore
  Heterogeneous Single-Core enables fine-grained thread swapping.
  MeoMean of each benchmark when paired with all benchmarks
  Zero migration time and perfect performance prediction for both.
  Heterogeneous multicore is unfair  Good for baseline

## Slide 6: Performance Prediction
Predictors in Pervious Heterogeneous Single Core Architecture
  Determine one thread P/E-backend
  Binary classification based on architecture status
    e.g. cache miss rate, PB miss rate
Needs to Schedule 2 Threads
  A more complex model needed
  Our simulation shows that the previous algorithm does not fit
  Keep fairness as well as performance
  Need new performance predictor for scheduling
The hardware can determine when turn off all migration
  Needs to predict IPC of both workloads on P/E backends

## Slide 7: Challenges in Heterogeneous Single-Core Workloads
When schedule same workload
  threads in equivalent phases, limits speedup
  Like in pervious figures
When schedule distinct workloads
  Differences in program characteristics can outweigh the diversity in phases.
The combination of some threads yields good performance
  Pairing certain threads can lead to enhanced performance
    Advanced OS algorithms needed
  Constraints on Heterogeneous Single-Core Systems
  Needs to simplify the task of identifying workloads

## Slide 8: Contributions
Heterogeneous Hyperthreading
  Extend the previous single-core heterogeneous architecture
  Enable simultaneous multi-threading on both backends
  Maintain grained thread scheduling with better utilization
History Based Performance Predictor
  Improve Prediction accuracy by caching previous performance
  Yield better schedule compare with previous work
Phase-shifted Batched Execution
  Schedule similar threads with a phase-change
  Similar threads are common in servers and multithread programs
  Reduce the effort of the OS to find suitable workloads
Thread Switching Mechanism
  Minimized stall on P-backend at the expense of E-backed stall

## Slide 9: Heterogeneous Hyperthreading Architecture
  Share resource as Hyperthreading, but Heterogeneous

## Slide 10: History Based Performance Predictor
  Predict IPC for next scheduling window with previous IPC

## Slide 11: Optimized Thread Migration
  Minimized stall on P-backend

## Slide 12: Methodology
GEM5 in X86 + Modifications
  Intel Skylake architecture config -> P-Backend
  Intel Skylake architecture config scale down > E-Backend
    Same scale down in Alderlake architecture E-core
  In-order core similar to ARM.
SpecCPU 2006 and Redis + YCSB
Considered the overhead of Hyperthreading

## Slide 13: Speedup with Intel Config

## Slide 14: History Based Performance Predictor

## Slide 15: Phase-shifted Batched Execution

## Slide 16: Fairness in Scheduling
  Heterogeneous Hyperthreading achieve fair scheduling

## Slide 17: Power and Area
Power and Area estimation with McPAT + Cacti.
  In 40 nm technology
  Heterogeneous Hyperthreading incurs 6% area overhead

## Slide 18: Conclusion
Heterogeneous Hyperthreading improve the hardware utilization of single core Heterogeneous architecture
All contributions improved the performance
  Heterogeneous Hyperthreading
  History Based Performance Predictor
  Phase-shifted Batched Execution
  Thread Switching Mechanism
Heterogeneous Hyperthreading achieves 18% speedup compare with Heterogeneous multicore with 6% of overhead

## Slide 19
Thank you
  Acknowledgement
Mingxuan He would like to say thank you to his colleagues at Futurewei for their invaluable assistance, insightful brainstorming sessions, and diligent proofreading throughout this project.
Mingxuan He would particularly acknowledge Dr. Sang Wook Stephen Do for his guidance and mentorship.